全對稱互補的A類耳機放大器

發表日期：2003年3月1日  出處：Sam Electronic Circuits  作者：L hood

電路圖如下:

元件的選擇：

| R1-4= 1K2 | R12= 4R7 | C8-10= 470uF 25V |
| --- | --- | --- |
| R2-3= 3K9 | RV1= 10K Log. pot. | C9-11= 100nF 100V ceramic |
| R5-10= 10K | TR1= 10K Trimmer | Q1-3= BC184 |
| R6=100K | C1= 4.7uF 63V MKT | Q2-4= BC214 |
| R7-9= 2K2 | C2-7= 100uF 25V | Q5= BD136 or BD538 |
| R8= 150R | C3-5= 100nF 100V MKT | Q6= BD135 or BD537 |
| R11-13= 6R8 | C4-6= 100uF 16V | All resistors is 1/4W 1% |

技術參數：

It is a very useful thing , to have a small headphone amplifier , capable of driving a couple of pairs phones. Fortunately, the headphone amp has a much easier job to do, in that neither the output power requirements nor the load characteristics are so severe, since headphones typically have a load, impedance , higher of 50 ohm, (typical 600 ohm), and only require 1-2V RMS. max, for normal output. Since only a low power output is required, a Class A stage, is perfectly feasible. For adequate Class A operation the output transistors Q5-6, should pass say 100mA each. With ±15V supply this would mean 1.5Watts dissipation, so a smallish Heatsink, will be needed for each. With RV1 adjust input audio signal and Tr1 adjust the output DC Offset voltage for 0V (±30mV). For stereo application , you need two unit, of this amp. by L. Hood

Sam Electronic Circuits 8/01